## Slide 1: PENGERINGAN

## Slide 2
Terminologi untuk penghilangan kadar cair (moisture content) yang relatif sedikit dari suatu zat
Secara umum hasil berupa ‘solid product’
  Bentuk/wujud Hasil Pengeringan
  •serpih (flake),
  •bijian (granule),
  •kristal(crystal),
  •serbuk(powder),
  •lempeng(slab), atau
  •lembaran sinambung (continous sheet)
Proses dilakukan pada kondisi di bawah titik didih air
Bukan proses yang melibatkan mekanik, seperti pengurangan kadar air menggunakan centrifuge
Pengeringan biasanya merupakan tahap akhir dari suatu proses

## Slide 4: Karakteristik pengeringan : equilibrium moisture content
Bahan yang higroskopis akan mempunyai kandungan air tertentu apabila dikontakkan dengan udara yang mempunyai temperatur dan suhu tertentu
Disebut sebagai ‘equilibrium moisture content’

## Slide 5: Karakteristik pengeringan : equilibrium moisture content
Variation of relative humidity with equilibrium moisture content for different materials

## Slide 7: Karakteristik pengeringan : equilibrium moisture content
Selalu terdapat : hysterisis
Kurva setimbang yang berbeda saat diperoleh dari proses yang berbeda : dengan absorpsi atau desorpsi

## Slide 8: DEFINISI : 1. Moisture content, basis basah = Kg moisture x 100 % Kg padatan basah Kg moisture x 100% Kg padatan kering + kg moisture
2. Moisture content, basis kering = Kg moisture x 100 % Kg padatan kering

## Slide 9: 3. Equilibrium moisture (X*) : moisture content padatan ketika pada kondisi kesetimbangan dengan tekanan parsial uap tertentu. 4. Bound moisture : moisture content padatan yang memberikan tekanan uap kesetimbangan kurang daripada tekanan uap cairan murni pada temperatur tertentu. 5. Unbound moisture : moisture content padatan yang memberikan tekanan uap kesetimbangan sama dengan tekanan uap cairan murni pada temperatur tertentu. 6. Free moisture : moisture content padatan yang berlebih dibanding dengan equilibrium moisture content sebesar X - X*. Hanya free moisture yang bisa diuapkan.

## Slide 11: OPERASI PENGERINGAN
Operasi pengeringan bisa diklasifikasikan batch atau kontinyu.
Klasifikasi didasarkan pada bahan yang dikeringkan.
Pengeringan batch (dalam kenyataannya semi batch): sebanyak bahan tertentu dikeringkan pada aliran udara yang mengalir.
Pengeringan kontinyu : baik bahan maupun udara pengering dialirkan secara kontinyu.
Klasifikasi peralatan pengeringan :
1. Metode operasi : batch atau kontinyu.
2. Metode pemberian panas :
- Direct drier : gas panas dikontakkan langsung dengan bahan.
- Indirect drier : misalnya melalui konduksi lewat dinding logam
3. Sifat bahan yang dikeringkan : padatan, butiran.

## Slide 12: Kecepatan pengeringan
Untuk tujuan pengeringan tertentu :
  Estimasi ukuran dryer
  Kondisi udara pengering (kelembaban dan suhu)
  Waktu yang diperlukan
Percobaan pengukuran laju pengeringan
  Sampel diletakkan dalam tray
  Tray diletakkan dalam kabinet atau duct dimana udara dengan kondisi tertentu mengalir
  Pengurangan berat diukur dalam selang waktu tertentu

## Slide 13
Laju pengeringan R adalah
  R = kg H2O/m2.jam
  Ls= kg padatan kering
  A= luas permukaan pengeringan, m2
Atau menggunakan persamaan
Misal
Nilai ini diplot pada rerata konsentrasi
Kurva laju pengeringan diplot sebagai X vs R

## Slide 14: Kurva laju pengeringan untuk kondisi pengeringan konstan
Data :
Berat total pada berbagai waktu
Data diubah menjadi data laju pengeringan
Pada kondisi pengeringan tertentu maka diperoleh X*
Sehingga diperoleh free moisture content, X

## Slide 15
Slope dari suatu garis singgung pada t tertentu adalah
Laju pengeringan
atau
Nilai R ini diplot pada rerata kadar air

## Slide 16
KURVA PENGERINGAN
Point A’ : hot solid
Point B-C: constant-rate drying period in which surface of the solid remains saturated with liquid because the movement of water vapour to the surface equals the evaporation rate. Thus the drying rate depends on the rate of heat transfer to the drying surface and temperature remains constant. Surface temperature  TW
Point AB :
Warming up (unsteady) period where the solid surface conditions come into equilibrium with the drying air.
Before drying can begin, a wet material must be heated to such a temperature that the vapor pressure of the liquid content exceeds the partial pressure of the corresponding vapor in the surrounding atmosphere.
Point C : critical free moisture content, XC , where the drying rate starts falling and surface temperature rises. Insufficient water on surface

## Slide 17
Point C-D : first falling-rate drying period which surface is drying out. Rate of water to surface is less that rate of evaporation from surface
Point D : surface completely dry
Point D-E : second falling-rate period in which evaporation is from inside of solid.
Point E : equilibrium moisture content, X*, where no further drying occur

## Slide 18: Perhitungan constant rate periode

## Slide 19
t1 =?
t2 =?

## Slide 20
Rc = 1,51

## Slide 21: Perhitungan falling rate periode

## Slide 22: Falling rate periode : special case

## Slide 23: Falling rate periode : special case
b) Rate is a linear function thru’ origin (a straight line from C to E at the origin)
Rc
Xc

## Slide 24
PREDICTING CONSTANT RATE OF DRYING PERIOD
Predicted mass-and-heat coefficients:
Mass transfer of water vapour
Steady-state : rate of mass transfer = rate of heat transfer
To determine the time required for drying from X1 to X2:
Heat transfer furnishes the latent heat of evaporation
Assumptions:
Only convective heat transfer to solid surface from hot gas to surface
Mass transfer is from surface to hot gas
Notes: 24

## Slide 25
where
A = exposed drying area (m2)
W = latent heat at TW (J/kg)
Rate of drying, RC:
T, TW = temp. of gas & surface of solid, respectively (oC)
MA,MB = molecular weight of water & air, respectively
h = heat-transfer coefficient (W/m2.K)
Hw, H = absolute humidity, kg H2O/kg dry air
Notes: 25

## Slide 26
Air flowing parallel to the drying surface (T = 45-150oC, G = 2450 -29300 kg/h.m2,  = 0.61-7.6 m/s)
h = 0.0204G0.8
Air flowing perpendicular to the drying surface (G = 3900 -19500 kg/h.m2,  = 0.9-4.6 m/s)
h = 1.17G0.37
where G = mass velocity =
To determine the time required for drying from X1 to X2:
Notes: 26

## Slide 30: Contoh
A granular insoluble solid material wet with water is being dried in the constant-rate period in a pan 0.61m x 0.61m and the depth of material is 25.4 mm. The sides and bottom are insulated. Air flows parallel to the top drying surface at a velocity of 3.05 m/s and has a dry bulb temperature of 60oC and a wet bulb temperature of 29.4oC. The pan contains 11.34 kg of dry solid having a free moisture content of 0.35 kg H2O/kg dry solid, and the material is to be dried in the constant-rate period to 0.22 kg H2O/kg dry solid.
  a) Predict the drying rate period and the time in hours needed.
  b) Predict the time needed if the depth of material is increased to 44.5 mm

## Slide 31: JENIS ALAT PENGERING

## Slide 33: Batch dryer
Digunakan untuk kapasitas produksi di bawah 50 kg/jam

## Slide 34: Tray Dryers
In tray dryers, the food is spread out, generally quite thinly, on trays in which the drying takes place.
Heating may be by an air current sweeping across the trays, by conduction from heated trays or heated shelves on which the trays lie, or by radiation from heated surfaces.
Most tray dryers are heated by air, which also removes the moist vapours.

## Slide 36: Continuous dryer
Untuk kapasitas produksi di atas 1000 kg/jam

## Slide 37: Tunnel Dryers
These may be regarded as developments of the tray dryer, in which the trays on trolleys move through a tunnel where the heat is applied and the vapours removed.
In most cases, air is used in tunnel drying and the material can move through the dryer either parallel or counter current to the air flow.
Sometimes the dryers are compartmented, and cross-flow may also be used.

## Slide 38: Roller or Drum Dryers
In these the food is spread over the surface of a heated drum.
The drum rotates, with the food being applied to the drum at one part of the cycle.
The food remains on the drum surface for the greater part of the rotation, during which time the drying takes place, and is then scraped off.
Drum drying may be regarded as conduction drying.

## Slide 39: Fluidized Bed Dryers
In a fluidized bed dryer, the food material is maintained suspended against gravity in an upward-flowing air stream.
There may also be a horizontal air flow helping to convey the food through the dryer.
Heat is transferred from the air to the food material, mostly by convection.

## Slide 40: Spray Dryers
In a spray dryer, liquid or fine solid material in a slurry is sprayed in the form of a fine droplet dispersion into a current of heated air.
Air and solids may move in parallel or counterflow.
Drying occurs very rapidly, so that this process is very useful for materials that are damaged by exposure to heat for any appreciable length of time.
The dryer body is large so that the particles can settle, as they dry, without touching the walls on which they might otherwise stick.
Commercial dryers can be very large of the order of 10 m diameter and 20 m high.

## Slide 41: Pneumatic Dryers
In a pneumatic dryer, the solid food particles are conveyed rapidly in an air stream, the velocity and turbulence of the stream maintaining the particles in suspension. Heated air accomplishes the drying and often some form of classifying device is included in the equipment. In the classifier, the dried material is separated, the dry material passes out as product and the moist remainder is recirculated for further drying.

## Slide 42: Rotary Dryers
The foodstuff is contained in a horizontal inclined cylinder through which it travels, being heated either by air flow through the cylinder, or by conduction of heat from the cylinder walls. In some cases, the cylinder rotates and in others the cylinder is stationary and a paddle or screw rotates within the cylinder conveying the material through.

## Slide 43: Bin Dryers
In bin dryers, the foodstuff is contained in a bin with a perforated bottom through which warm air is blown vertically upwards, passing through the material and so drying it.

## Slide 44: Belt Dryers
The food is spread as a thin layer on a horizontal mesh or solid belt and air passes through or over the material.
In most cases the belt is moving, though in some designs the belt is stationary and the material is transported by scrapers.

## Slide 45: Vacuum Dryers
Batch vacuum dryers are substantially the same as tray dryers, except that they operate under a vacuum, and heat transfer is largely by conduction or by radiation. The trays are enclosed in a large cabinet, which is evacuated. The water vapour produced is generally condensed, so that the vacuum pumps have only to deal with non-condensible gases. Another type consists of an evacuated chamber containing a roller dryer.

## Slide 46: Freeze Dryers
The material is held on shelves or belts in a chamber that is under high vacuum. In most cases, the food is frozen before being loaded into the dryer. Heat is transferred to the food by conduction or radiation and the vapour is removed by vacuum pump and then condensed. In one process, given the name accelerated freeze drying, heat transfer is by conduction; sheets of expanded metal are inserted between the foodstuffs and heated plates to improve heat transfer to the uneven surfaces, and moisture removal. The pieces of food are shaped so as to present the largest possible flat surface to the expanded metal and the plates to obtain good heat transfer. A refrigerated condenser may be used to condense the water vapour.