## Slide 1: PRODUCT DEVELOPMENT TO BUSINESS
Part 2

## Slide 2
Nylon: Centralized Development
Exploration-Discovery Phase
The story began in December 1926, when the director of the Chemistry Department, Charles Stine, submitted to the Executive Committee of DuPont a short memorandum entitled “Pure Science Work”.
After he received approval and funding from his management, he went about recruiting outstanding research chemists, but by February 1928 he had recruited only one man, a 31-year-old instructor from Harvard named Wallace Hume Carothers.
The nature of polymers was still being debated, and the Nobel Prize in Chemistry for Hermann Staudinger came decades later in 1953, for his proposal in the early 1920s that polymers are long chains of monomers held together by ordinary chemical bonds.
Carothers supported this point of view, and proposed a scheme to prove it. He proposed to build long-chain molecules one step at a time, by carrying out well-understood chemical reactions.

## Slide 3
Nylon: Centralized Development
His scheme was to react dihydric alcohol molecules with –OH groups on both ends, together with diacid molecules with acid groups on both ends, to make a polyester of potentially unlimited length.
He and Julian Hill, a member of his research group, were able to make chains with a molecular weight of 5000 to 6000, and he called them “condensation polymers.”
In April 1930, they heated a16-carbon diacid with a three-carbon dihydric alcohol, removed the product from the still, and found a molten polyester with a molecular weight of 12,000. They made an unexpected discovery: after cooling, this fiber could be stretched or “cold drawn” into very strong fibers. However, they found that this 3–16 fiber was not suitable as a textile fiber because it melted below 100 ◦C, was partially soluble in dry-cleaning solvents, and was sensitive to swelling in water. The discovery was made in April 1930, and the long journey of development and commercialization would take 10 years before nylon became generally available for sale as stockings.

## Slide 4
Nylon: Centralized Development
This all-synthetic fiber has different properties from the semi-synthetic rayon, as it retains nearly all its strength when wet and has an elasticity that only silk can match.
Their next move was to switch from dihydric alcohols to diamines, which react with a diacid to form a polyamide, as they knew that simple amides have higher melting temperatures than the corresponding simple esters. However, the desirable properties for a textile fiber of high melting point and low solubility in water and solvents would also make it difficult to spin into fibers before knitting into fabrics.
The work was halted in the middle of 1933, due to the inability to find ways of making progress, until it was taken up again early in 1934 by his assistant Donald D. Coffman. In March 1934, Coffman drew a fiber from 4 g of polymer that he had made, and heated it in a bath at 200 ◦C, just above its melting point, and drew a lustrous filament of polyamide fiber. That was the first nylon fiber. Not long after that, Carothers went into an unusually severe depression and was hospitalized for a while.

## Slide 5
Nylon: Centralized Development
Development Phase
From the day that Hill pulled the first polyester fiber, DuPont focused its energies on creating a synthetic fiber, instead of polymer resins or rubber. An early decision was made to concentrate only on full-fashioned silk hosiery. A silk stocking contains only 10 g of resin, but a wool sweater consumes much more resin and would require a much larger plant investment. At that time, $70 million worth of silk went into stockings each year, which were knitted into eight pairs of stockings per American consumer per year.
The tasks of development and commercialization were formidable. The technology to manufacture the intermediate chemicals and the technology of spinning the polymer into fibers had to be developed.
The numerous small textile mills that knit silk into stockings were incapable of adapting to knitting nylon, as they did not have the staff and the technical capabilities to do new product development, and they were not used to large-scale advertising to educate and persuade customers.
DuPont was able to undertake the development, as it had the necessary resources and connections: its Ammonia Department had experience with high-pressure catalytic reactions, and its Rayon Department had experience in manufacturing and selling to the textile business.

## Slide 6
Carothers collected much physical, chemical, and mechanical data on the fibers, but he did not know how the data correlated with “ultimate practical behavior” and performance to the satisfaction of consumers.
In the summer of 1934, his group also had to determine which combination of diacid and diamine would be the best, within the range from 2 to 10 carbon atoms. The initial focus was on the 5–10 polymer; enough polymers were made to spin into fibers and made into fabrics and then sent to the Rayon Department for testing. It is easy to polymerize and spin 5–10, but it melted at 190 ◦C, so that it could not withstand practical ironing temperatures.
Gerald J. Berchet prepared nylon 6–6 in February 1935, which would become the commercial product. This nylon 6–6 melts at over 250 ◦C, which is excellent. It is even more important that the raw material comes from benzene, which in turn comes from easy to obtain coal tar or petroleum refining.
They still had to solve the problem of the commercial production of the two starting materials, namely adipic acid and examethylenediamine. But the difficulty was greater in the spinning process, which could be carried out either from a solution, or from a melt at above 260 ◦C.
Nylon: Centralized Development

## Slide 7
Nylon: Centralized Development
The Chemical Department made the decision to develop nylon 6–6 in July 1935.
The process to make hexamethylenediamine required a multistep synthesis, involving: hydrogenating benzene to make cyclohexane, which was oxidized to make a mixture of cyclohexanone and cyclohexanol, which was oxidized to adipic acid (one of the components of nylon 6–6). Half of the adipic acid was catalytically reacted to make adiponitrile, which was hydrogenated to make hexamethylenediamine (the other component of nylon 6–6).
Several batches of the order of a few pounds of intermediates were needed to do the polymerization reaction. Melt spinning procedures at a temperature of about 260 ◦C were developed. By the summer of 1936, DuPont became confident that they could make nylon yarn at a cost of 80¢ per pound in a plant of 8 million pounds capacity, which could be sold at $2.00 per pound at roughly the price of silk.
They decided to expand the manufacturing capacity from 2 lbs to 100 lbs a day to improve confidence in the process, and to provide material for extensive field testing.
In February 1937, a batch of yarn was taken for a knitting test at the Union Manufacturing Company in Maryland; the results were unsatisfactory, as the product did not come off the spools easily, snagged at knitting machines, and looked like a wrinkled mess with an unpleasant gray color.

## Slide 8
Nylon: Centralized Development
In the meantime, the mental condition of Carothers deteriorated inexorably. He was elected to the National Academy of Sciences in 1936. But he had another breakdown in the summer of 1936, and finally, in April 1937, he committed suicide with cyanide in a Philadelphia hotel room.
At Christmas 1937, the Van Raalte Mill in New Jersey finally turned out “full-fashioned hosiery with excellent appearance and free of defects.” They distributed 56 hosiery and lingerie garments to wives of the men on the nylon project. The majority of the women thought that the stockings were very durable, but they wrinkled too easily and were too lustrous and slippery.

## Slide 9
Nylon: Centralized Development
Commercialization and business phase
The Executive Committee of DuPont authorized a pilot plant on January 1938, which took 6 months to build and another 6 months to provide sufficient data to help in the construction of a commercial plant.
In October 1938, the Executive Committee allocated $8.5 million to build a 4 million pound a year plant at Seaford Delaware, which began operation in January 1940.
Charles Stine announced this new product in October 1938 at the New York World’s Fair to 3000 members of a women’s club. He said: This textile fiber is the first man-made organic textile fiber prepared wholly from new material from the mineral kingdom. . . . Though wholly fabricated from such common raw material as coal, water, and air, nylon can be fashioned into filaments as strong
as steel, as fine as spider’s web, yet more elastic than any of the common natural fibers.
Nylon finally became available to the general public in May 1940. Ten years had passed from initial discovery to full commercialization. It was a tremendous effort, even for a company with the resources of DuPont, and the R&D cost was $4.3 million.
During World War II, DuPont nylon production went up to 25 million pounds a year, and was used to make parachutes, airplane tire cords, and glider tow ropes. DuPont resumed selling nylon for stockings after the war.

## Slide 10
Penicillin: Distributed Development
Alexander Fleming said (Nobel e-museum 2002):
It arose simply from a fortunate occurrence which happened when I was working on a purely academic bacteriological problem which had nothing to do with antagonism, or molds, or antiseptics, or antibiotics.
In my first publication I might have claimed that I had come to the conclusion, as a result of serious study of the literature and deep thought, that valuable antibacterial substances were made by molds and that I set out to investigate the problem. That would have been untrue and I preferred to tell the truth that penicillin started as a chance observation.
My only merit is that I did not neglect the observation and that I pursued the subject as a bacteriologist. My publication in 1929 was the starting-point of the work of others who developed penicillin, especially in the chemical field. . . .
We tried to concentrate penicillin, but it is easily destroyed, and to all intents and purposes we failed. We were bacteriologists—not chemists—and our relatively simple procedures were unavailing.

## Slide 11
Exploration–Discovery Phase
Penicillin: Distributed Development
It began as an accidental discovery and observation that lay dormant for many years,as the discoverer lacked the means and connection to develop a product with sufficient quantity and purity to be used in clinical use. It laid dormant until another team appeared on the horizon, and it took World War II to provide the motivation and the resources critical to its development before penicillin became the life saver for millions.
Penicillin, the first and still one of the most widely used antibiotic agents, is derived from the Penicillium mold. Alexander Fleming was a Scottish bacteriologist who took his degree at St Mary’s Hospital Medical School of London University and continued his research in the Royal Army Medical Corps in World War I.
In 1928, Fleming was working with Staphylococcus bacteria, and was growing colonies in Petri dishes in his musty, dusty, and none too tidy laboratory. After a vacation, he observed in a Petri dish that colonies of the bacterium Staphylococcus aureus failed to grow in rings around areas that had been accidentally contaminated by the green mold Penicillium notatum.
He found a substance in the mold that prevented growth of the bacteria even when it was diluted 800 times, which he called penicillin. Penicillin works by inhibiting the bacterial enzymes responsible for cell-wall synthesis, and activating other enzymes to break down the organism’s protective walls.

## Slide 12
Penicillin: Distributed Development
The work lay dormant for 12 years, until the German fire-bombing of London in World War II, when an Oxford group began searching for new antibacterial drugs for burns treatment. Howard Florey was an Australian pathologist who studied medicine at Adelaide and Oxford and became a professor of pathology at Oxford in 1935.
Ernst Chain was a German-born biochemist who studied chemistry and physiology in Berlin and fled to England to work with Florey at Oxford. They were also encouraged by the news of the success of the new sulfa drugs of Gerhard Domagk.
In 1939, they studied a number of antibacterial substances and decided to concentrate on the penicillin mold, making an injectable form of the drug. They demonstrated its therapeutic effectiveness on mice, and then on humans suffering from Staphylococcus. But it was clear that wartime England did not have the resources to develop large-scale industrial production of penicillin.

## Slide 13
Penicillin: Distributed Development
Commercialization: Business Phase
In the human body, natural penicillin breaks down under acidic conditions as it passes through the stomach, so semi-synthetic penicillin was developed that is more acid stable and can be given in oral medication. Penicillin has significant side effects, in causing allergic or hypersensitivity reactions, including skin rashes, hives, swelling, and anaphylaxis or allergic shock.
Scale-Up Progress
1943 1.7 billion units/month
1944 138.0 billion units/month
1945 570.0 billion units/month